## Slide 1
The ISOLPHARM Project
New method for production of high specific activity
radionuclides as radiopharmaceutical precursors
Alberto Andrighetto
INFN – Laboratori di Legnaro

## Slide 2
The SPES project at LNL
Radiopharmaceutical production
ISOLPHARM: a new method based on ISOL technique
Innovative radio-isotopes for nuclear medicine
Experimental activities
Conclusions
Talk Overview

## Slide 3: The SPES at LNL: Facility Layout
Project financied by INFN
New infrastructure for:
Application Facility
Cyclotron
RIB facility (2th generation ISOL)
New Building:
Notes: Unico punto in cui si parla di building&infrastr., poi c’è la visita.
E’ stato realizzato l’edificio per il ciclotrone, le stazioni di irraggiamento ISOL e per le aree applicative, il sistema di selezione in massa. Il nuovo edificio è collegato all’edificio ALPI.
The new building has a surface of almost 3600 mq with an underground level connected to the third experimental hall and the ALPI building. The beam transport, together with the CB and the Medium Resolution Mass Separator, will be mounted inside the third exp hall and the RFQ will be inside the ALPI building.

## Slide 4
SPES-RIB (ISOL): main apparatus
1 - Driver:
Best Theratronics cyclotron
3 - Post Accelerator:
Alpi existing complex
ALPI
4 – RIB production source:
NEW CONCEPT
(Multi-foil UCx target)
Target-Ion Source Complex:
optimized for 8kW beam power
- Eproton = 40 MeV for RIB
10^13 fission/s.
2 - RIB manipulation
Mass Separator (WF)
Beam Couler
HRMS
Charge Breeder
RFQ
Notes: 12/06/2017
4

## Slide 5
TIS unit
horizontal handling device
vertical handling device
front-end
temporary storage
PROTON BEAM
RIB
The SPES RIB source

## Slide 6
The TIS UNIT (general scheme)
Ions
Fission fragments
Primary beam
Primary beam
Production target
Transfer Line
Extraction Electrode (GND)
Ion Source (+HV)

## Slide 7: Project construction phases (RIB facility)
Exp. areas
Beam cooler
MRMS
ALPI
RFQ
1+ Exp. areas
CB
HRMS
Target
Cyclotron
PIAVE
XTU-Tandem
LRMS
Phase 3
Phase 1.
Phase 2.
Phase 2.
Phase 3.
Phase 1. - Building + First operation with the cyclotron
Phase 2. - From C.B. to RFQ + SPES target, LRMS, 1+ Beam Lines
Phase 3. - From the LRMS to the CB + rom RFQ to ALPI
2) RIB production area
3) Beam Manipulation area
4) Post acceleration area
1) Driver
Notes: Se anche tu la fase 3 la splitti in due lo faccio anch’io: mi sembra più logico, di fatto sono due pezzi di macchina diversi, come per le fasi 2a e 2b

## Slide 8
SPES is: 1) A second generation ISOL facility (for neutron-rich ion beams)
2) An interdisciplinary research center (for p,n applications)
SPES: Is the future of LNL
Cyclotron installation & commissioning:
E=70 MeV proton beam, I= 750 mA
LARAMED & ISOLPHARM projects
Radisotopes for medical applications
Production & re-acceleration of exotic beams, from p-induced Fission on UCx
Accelerator based neutron source
(Proton and Neutron Facility for Applied Physics)
SPES for medicine
SPES-RIB facility
Financed
Financed &
Under construction
Proposal
SPES-DRIVER
In commissioning
SPES Neutron facility

## Slide 9
ISOLPHARM at LNL
A innovative method for medical applications
+
+
+
+

## Slide 10
Radionuclides properties:
Decay properties
Half-life
Chemical properties
Production Feasibility
Radiopharmaceuticals are medicines that deliver a predefined amount of radiation to a target tissue for diagnostic or therapeutic purposes
Therapeutic agents
Diagnostic agents
What is a radiopharmaceutical?
They are made of a “radioactive core” and a “carrier system”, the latter allows the deposition of radiation onto the malignant cell population and avoids damage to healthy tissues

## Slide 11
Carrier-free radionuclides
(high specific activity).
The specific activity is a measure of the activity per mass -> GBq/mg (or Ci/mg).
The Specific activity
A) Radionuclides diluted by isotopic impurities of the same element
B) Radionuclides without other isotopic impurity
Carrier-added radionuclides
(low specific activity).
Carrier free radionuclides are ideal to achieve high binding affinities to the receptors.
Only few sites are available on the cells -> optimization of radionuclide action !

## Slide 12
High neutron/proton fluxes required
Irradiation of targets of the same element
Direct reaction methods -> A(p,x) or A(n,x)…
Target with large activation levels
Chemical separation required
→ Isotopic impurities (Low S.A.)
2 main traditional methods
Cyclotron
Nuclear reactor
With ISOL technique:
Radionuclides can be easily produced as carrier-free isotopes (Mass Separation)
No nuclear reactor required for several beta- radionuclides
Production Methods

## Slide 13
The ISOL scheme: 4 stages
Beam Manipulations: Beam Cooler, Charge Breeding,
HRMS
RIB Source
DRIVER
Post-Accelerator
Beam Separation

## Slide 14
ISOLPHARM Method overview
The ISOLPHARM method is capable of selecting and isolating a
SINGLE RADIO-ISOTOPE
ISOL
PHARM
The ISOLPHARM patent
(EU + USA * Canada)
→ extremely high specific activity
→ the higher efficacy in therapy and diagnosis

## Slide 15
Radiopharmaceutical In the ‘market’ | Targeted organs | Half-life | Specific Activity (GBq/mg) # | 
 |  |  | ISOLPHARM technique production | Neutron capture reaction (Φ = 1014 cm-2s-1)
89Sr-SrCl2 | Bone | 50.5 d | ≥ 597 | ≥ 0.004
90Y-YCl3 | Liver and endocrine system | 64.1 h | ≥ 9480 | ≥ 0.8*
125I-NaI | Prostate, brain, lung, pancreas, liver | 59.4 d | ≥ 552 | ≥ 6
131I-NaI | Thyroid | 8.02 d | ≥ 3911 | ≥ 0.7
Radiopharmaceutical | Targeted organs | Half-life | Specific Activity (GBq/mg) | 
 |  |  | ISOLPHARM technique production | 235U fission
133Xe | Lung and liver | 5.25 d | ≥ 6920 | ≥ 3
High specific activity
Essential for the radioisotope conjugation to in-vivo carriers for targeted drug delivery
ISOL vs others : specific activity
*Non carrier added 90Y is also available from generators
# Ref: http://www.nupecc.org/pub/npmed2014.pdf -> (NuPECC) – Report of Nuclear Physics for Medicine

## Slide 16
Strontium-89 is a neutron-rich nuclide, with a l half-life of 50.5 days
Large Yields in the 238U(p,fission)89Sr reaction -> (p=40 MeV)
It is a pure beta emitter -> ( easy working processes )
All the isotopes of mass 89 quickly decay to Strontium-89.
A simple and effective mass separation will allow the production of a carrier-free strontium-89 isotope (further chemichal separation is not neccessary)
The ‘lucky’ case of 89Sr
89Rb = 15 min
89Kr = 3 min
89Br = 4 sec.
89Se = 0,4 sec.
89Sr Parents:

## Slide 17
Traditional methods (reactor)
Neutron capture of 88SrCO3 targets
ISOLPHARM method
Large Isotopic contamination in the substrate (88Sr)
Low Isobaric contamination in the substrate
Difficult chemical separation
Easy (No) chemical separation
Low specific activity
High specific activity
~ 597 GBq/mg
~ 0,004 GBq/mg
89Sr Production routes
238U(p, fission)89Sr
88Sr(n, γ)89Sr

## Slide 18
Treatment of bone metastatic pain secondary to prostatic carcinoma as 89SrCl2
Current use of
Strontium-89 chloride
(Metastron)
Application of 89SrCl2
ISOLPHARM method
Strontium-89 chloride
(Carrier-free)
Possible (?) new applications:
Radiolabeling of molecules that are directed towards specific receptors on the cells!
-> need to have carrier-free radionuclides!!

## Slide 19
ISOLPHARM 1: produced radionuclides at SPES
(Fluka estimation)
In target production of 89Sr and 90Y* using a standard UCx target
Already developed and tested!
In target production of 64Cu using a Ni-based target
Under development

## Slide 20
Towards ISOLPHARM2.
Targets R&D , estimated isotopes production
of innovative radio-isotopes for medicine
+
+
+
+

## Slide 21
ISOLPHARM 1 & 2
ISOLPHARM 1
First set of isotopes studied in the framework of ISOLPHARM collaboration:
radiopharmaceuticals available in the market
ISOLPHARM 2
Innovative radio-isotopes produced with different types of target
radiopharmaceuticals absent in the market

## Slide 22
SPES UCX target yield: other useful isotopes?
[nuclide/s]
ISOLPHARM 1 isotopes
Other ISOL isotopes?
ISOLPHARM 2
A lot of ISOL beams can be potentially produced:
Only a few of the produced isotopes are currently used/studied in nuclear medicine (traditional techniques allow the production of a limited variety of radioisotopes)
Is it possible that other isotopes will be interesting as radiopharmaceuticals “active core”?

## Slide 23
Other ISOL Isotopes of medical interest? (UCx)
Diagnosis
Theragnostics
Therapy
Selection criteria
Almost 60 ISOL isotopes were found!
(with different ISOL target)

## Slide 24
Innovative Target concepts: overview
  ⚛ UCX new targets (Operation temperature: 2200°C)
  ⚗ Target R&D and state of art:
  ☢ Innovative isotopes production: 111Ag
  ⚛ ZrGe target (Operation temperature: 1800°C)
  ⚗ Target R&D and state of art:
  ☢ Innovative isotopes production: As & Ga isotopes
  ☢ 64/67Cu unexpected production!
  ⚛ TiC/TiB2 target (Operation temperature: 2000°C)
  ⚗ Target R&D and state of art:
  ☢ Innovative isotopes production: Sc isotopes
The ISOL method requires specific targets.
Targets have to be:
  Solid
Refractory (more refractory than the element for which they were designed)
Three target concepts are currently under investigation:
Nuclear reactions studied
Designed
Tested
Nuclear reactions studied
Designed
Tested
Nuclear reactions studied
Designed
Tested

## Slide 25
The impact of ISOLPHARM 2 radionuclides
111Ag
Very good decay properties for the therapy
Half-life: 7.45 days
Emission: b- ; End-point energy 1036.8 keV, low associated g
Not produced as carrier-free so far!
Handbook of Nuclear Chemistry, Springer, DOI 10.1007/978-1-4419-0720-2
Great potential to become a new radionuclide for therapy!
64Cu/ 67Cu
64Cu -> very good PET radionuclide (diagnosys) Half-life: 12.8 hours
67Cu -> very good decay properties for therapy Half-life: 61.9 hours
Perfect matched pair -> diagnosys and therapy with the same element!
43Sc
PET radionuclide -> longer half life (~4 hours) than traditional PET (18F and 68Ga)
Better performance of tumors diagnostic procedures
Better than the 44Sc that has a hard associated g ray (~1 MeV) Half-life: 3,9 hours
Perfect matched pair with 47Sc (Therapeutic) Half-life: 3,3 days

## Slide 26
Main radionuclides for ISOLPHARM 2
(Fluka rate estimation)
111Ag
SPES UCx target PPB 40 MeV , 200 µA
64-67Cu
SPES ZrGe target PPB 70 MeV , 100 µA
43-44-47Sc SPES TiC target PPB 40 MeV , 200 µA

## Slide 27
ISOLPHARM
Experimental activities

## Slide 28
Simulation of the process using stable ion beams thanks to the SPES test bench (front-end off-line)
Beam deposition @ LNL
Ion beams produced, deposited, dissolved and analyzed: Sr+, Y+, I+, Cu+ (4 master, 2 PhD. students)
Activities @ UNIPD-DSF-DSC
Extraction from the substrate, quantification and chemical separation of the deposited element
Activity done so far at LNL - UNIPD-DSF

## Slide 29
ISOLPHARM collaboration
2014
2015
2016
2017
Field | Objective | Institutions
Nuclear physics | Generation and collection of nuclides | INFN-LNL
Radiochemistry | Chemical separation and complexation of the collected nuclides | UNIPD-DiSC
Radiopharmacy | Radiolabeling and in vitro/in vivo studies | UNIPD-DSF Reggio Emilia Hospital
Nuclear medicine | GMP development and possible clinical studies | Castelfranco Hospital

## Slide 30
The nuclides studied so far: ISOLPHARM 1
Element studied at LNL-PD | Radionuclide desired
Sr | 89Sr, 90Sr/90Y
Y | 90Y
I | 125I, 126I and 131I
Cu | 64Cu, 67Cu

## Slide 31
The proton driver

## Slide 32
The production targets
 | Standard (graphite) | Low density (MWCNTs)
Density (g/cm³) | 4.25 | 2.59
Diameter (mm) | 12.50 | 13.07
Thickness (g/cm²) | 0.41 | 0.41
Calculated porosity (%) | 58 | 75
UCx target already developed and tested on-line!
Other targets under development for specific radionuclides production
UCx target prototype
Porous titanium carbide (TiC)

## Slide 33
The ionization source
Ionized element | Desired radionuclide | Ionization source | Efficiency
Sr | 89Sr, 90Sr/90Y | SIS | ~ 20 %
Y | 90Y | PIS | ~ 1 %
I | 125I, 126I and 131I | PIS | ~ 20 %
Cu | 64Cu, 67Cu | PIS | ~ 10 %
Ag | 111Ag | PIS | ~ 6 %
Surface Ion Source (SIS)
Plasma Ion Source (PIS)
Copper Mass Scan (PIS)
63Cu (~70%)
65Cu (~30%)
Strontium Mass Scan (SIS)

## Slide 34
Beam acceleration and transport
Strontium and yttrium beams focalization
Electrostatic Triplets Quadrupoles and steereers system
Diagnostic boxes 1 and 2
(2 Faraday Cups and 2 Beam profilers)
Extraction -> 25 - 40 kV
Beam Transmission ~ 100%

## Slide 35
Isotope mass separator
Wien Filter
Natural Copper : Mass Scan
63Cu (~70%)
65Cu (~30%)

## Slide 36
Substrates for isotopes collection
For Sr, Y and Cu
Boiling point at 10-6 mbar
Sr ~ 500 °C
Y ~ 1500 °C
Cu ~ 1200 °C
1) Sodium Chloride
Sr1+ spot on the substrate
Cu1+ spot on the substrate
For I2
At 10-6 mbar I2 -> gas
2) Activated Carbon
40 mm
Polyvinyl Alcohol (PVA) as a binder

## Slide 37
Isotopes purification
2) Development of purification processes
Example: Separation of 90Sr from 90Y for 90Y purification
-> synthesis of an ion exchange inorganic material: sodium nonatitanate
1) Irradiated substrates dissolution and quantification of the deposed atoms
HNO3 0.1 M
Sr2+, Y3+ or Cu2+ quantification
via GF-AAS or ICP-AES
Iodine titration
Ongoing collaboration with UniPD-DSF and UniPD-DSC
Development of Seraparation Column for Y vs. Sr

## Slide 38
In vitro developments
2) Development of new targeting agents
1) Development of novel chelators for Ag+
Ongoing collaboration with:
TIFPA (Trento Institute for Fundamental Physics and Applications
DiSC (Department of Chemistry) UniPD
Ongoing collaboration with:
DSF (Department of Pharmaceutical and Pharmacological Sciences)
Nuclear Medicine Unit Advanced Technology Department (Santa Maria Nuova Hospital Reggio Emilia – IRCCS)
Radiolabeled molecule
Cancer cells
Novel molecules radiolabeled with innovative radionuclides as 111Ag

## Slide 39
ISOLPHARM
Conclusions.

## Slide 40
ISOLPHARM possible facility layout
Production target
Ion collection target
ISOLPHARM
Radioactive Ion Beam
Bunker ISOL 2
(ISOLPHARM)
Bunker ISOL 1
SPES
(nuclear physics)
Bunker 2 is currently empty..
New Budget is required for duplicated the ISOL source

## Slide 41
Summary
- At SPES it will be possible soon to produce radionuclides for medical purposes using the ISOL technique.
- The ISOLPHARM method (patent deposited) is focused on the production of radiopharmaceutical precursors with high specific activity using a proton beam ad intermediate energies.
- The ISOLPHARM collaboration is started 3 years ago. An increasing experimental activity is being carried out.
Some radionuclides (as 111Ag , 43Sc, etc) seem extremely interesting and could be used as precursors for new radiopharmaceuticals.
First step: to produce first radionuclides of medical interest for research (small quantities) when the first SPES RIB will be delivered.

## Slide 42
ISOLPHARM collaborating institutions
The Italian Network
The International Network

## Slide 43
Thanks for your attention!
& to the RIB production group..