## Slide 1: The influence of the “new” CRP on monitor reactions for charged particle beams. A. Hermanne (on behalf of all CRP participants)
Vrije Universiteit Brussel (VUB), 1090 Brussels, Belgium
Notes: Thanks to organising committee and chairman, attendance

## Slide 2: Monitoring of charged particle beams Technique to improve or confirm knowledge of beam intensity and/or energy. Activation analysis experiments and isotope production. Re-measurement of cross-sections (excitation function) of specific reactions on well-chosen targets. Comparison with evaluated-recommended values. Adapt beam parameters until good agreement. IAEA-database
Notes: Thanks to organising committee and chairman, attendance

## Slide 3: Example (recent study Ba+deuterons)
Notes: Thanks to organising committee and chairman, attendance

## Slide 4: Genesis of “new” recommended database The IAEA organized in the 1996-2001 period a CRP : first attempt to provide standard – recommended cross-section data for monitoring and for isotope production. The results available as hardcopy TECDOC-1211. On-line in the medical portal (latest update 2007) https://www.nds.iaea.org/medical/monitor_reactions.html End 2012 launch of a new CRP entitled: “Nuclear Data for Charged-particle Monitor Reactions and Medical Isotope Production“ Aim to complement, broaden and upgrade the database. An important goal was the improvement on accuracy and reliability of cross-sections for monitoring of proton, deuteron, alpha and 3He particle beams.
Notes: Thanks to organising committee and chairman, attendance

## Slide 5: New systematic compilation of literature, especially for recent, well documented published data. Performing dedicated experiments. Confirm excitation functions for the existing reactions Extend to a wider energy range. Special attention to correction of outdated nuclear data. Latest values for g-ray abundances and half-lives used. Checked – corrected subgroup evaluators nuclear data. For most beams several new reactions were added
Notes: Thanks to organising committee and chairman, attendance

## Slide 6: Added 46Sc formation on natTi for p and d (48V) Added reactions on Cu for d and 3He (Cu backings)
Notes: Thanks to organising committee and chairman, attendance

## Slide 7: Most important progress is introduction of uncertainties on the recommended cross-sections for all monitor reactions. Compilers provided total uncertainties on ALL experimental cross-section values. Based on values published by the original authors or on their experience with experimental techniques. Selected data series Statistical fit by the Obninsk group using Padé approximation. Recommended excitation functions with confidence interval. Reduced uncertainties compared to the original data sets. Adding a correction for systematic effects and correlations, overall uncertainties of the order of 5% on the individual recommended cross sections are obtained.
Notes: Thanks to organising committee and chairman, attendance

## Slide 8: natTi(d,x)48V (15.97 d)
12 references
New since 2007:
Gagnon(2010),Hermanne(2012), Khandaker (2014), Takacs (2013)
Deselected:
Burgus(1954), Chen(194),
Jung (1987), Takacs(1997)
Adapt uncertainties where necessary to have consistent data.
Padé fit
18 parameters
182 datapoints
c2 = 1.04
Notes: Thanks to organising committee and chairman, attendance

## Slide 9
Uncertainties (5% systematics)
12% at threshold
5-6% in 10- 50 MeV range
Lower than original experiments
Useful: 8- 40 MeV range
48Ti(d,2n)48V T = 7.32 MeV
Low energy bump
47Ti(d,n)48V Q = 4.60 MeV
Presence of 48Sc !!!!!
T1/2 = 43.67 h
Notes: Thanks to organising committee and chairman, attendance

## Slide 10
natTi(d,x)46Sc (83,79d)
New since 2007: All
12 Refs
Hermanne (2014): 16 sets
Deselected (7 sets)
Andres(1960), Chen (1964), Hermanne (2014) (j,k,p) Jung(1987), Takacs (1997)
Adapt uncertainties where necessary to have consistent data.
Padé fit ,
13 parameters,
372 datapoints,
c2 = 0. 78
Notes: Thanks to organising committee and chairman, attendance

## Slide 11
Uncertainties (5% systematics)
22% threshold
4.2 % in 12- 32 MeV range
4.8 % at 80 MeV
Lower than original
Useful 10- 80 MeV range
48Ti(d,a)48V Q= 3.97 MeV
High energy
48Ti(d,2p2n)48V
Q= 25.34 MeV
Notes: Thanks to organising committee and chairman, attendance

## Slide 12: Cu(p,x)62Zn (9.186h) Cu(p,x)63Zn (38.47 m)
Kellet: use ENSDF
Nichols: new evaluation
BIPM-5 2013 - library LNHB
Slight changes,
No reason for discrepancy
Short half life !!!
31 Refs. 5 new 11 deselected
c2= 1.035
10% threshold 4.7 % 7- 21 MeV
27 Refs. 9 new 7 deselected
c2= 1.91
15- 100 MeV
80% threshold
5.2% in 25- 40 MeV range
7.2% at 100 MeV
Notes: Thanks to organising committee and chairman, attendance

## Slide 13: natCu(3He,x)66Ga natCu(3He,x)65Zn
All new 5 Refs.
Golchert <15 MeV deselected
Only 65Cu in study, no low energy
Kondratev * 0.85
c2= 0.2
Uncertainty 20% near threshold
4.1% above 17 MeV
All new 6 Refs.
Golchert deselected
c2= 1.69
Uncertainty 30% threshold
Below 7% above 15 MeV
Notes: Thanks to organising committee and chairman, attendance

## Slide 14: The presence of the strongly discussed bump in the 27Al(p,x)22Na excitation function around 100 MeV was confirmed by TALYS calculations as results of the onset of the reactions with separate nucleons.
Up to 1000 MeV
34 Refs in total New 14 (previously < 100 MeV)
12 deselected
c2= 1.47
High energy protons : 27Al(p,x)22Na
Uncertainties 20% near threshold
< 4% in 45 – 800 MeV region
Notes: Thanks to organising committee and chairman, attendance

## Slide 15
TALYS calculation
Underestimation at max
Overestimation “bump”
Sum of all = Total= TENDL2015
Strongest at low energy (p,pna) not (p,da)
Bump = (p,3p3n)+(p,2p2nd)
Thresholds
52.7 and 50.4 MeV
Max. Contribution 5 mb
90-120 MeV
Notes: Thanks to organising committee and chairman, attendance

## Slide 16: Correction factor for the natMo(p,x)96Tc reaction, used as monitor in the systematic Levkovski study (1991) estimated : 0.8 by Takacs (2002) (measurement); 0.827 ± 0.05 by Qaim (2014) (comparison different reactions)
Cross-section at 30 MeV
Levkovski : 250 ± 10 mb CRP: 192.9 ± 8.4 mb
Correction factor 0.77 ± 0.07
13 References
One deselected
Not Levkovski data
c2= 1.34
Uncertainties
70% threshold
4.5- 6% up to 45 MeV
Notes: Thanks to organising committee and chairman, attendance

## Slide 17: Monitors only part of the CRP Diagnostic radionuclides (± 80 reactions) SPECT- g emitters b+ emitters - PET imaging generators (PET) Therapeutic radionuclides (± 30 reactions)
Notes: Thanks to organising committee and chairman, attendance

## Slide 18: A. Hermanne1, R. Capote2, B. V. Carlson3, J. W. Engle4, M. Hussain5, A. V. Ignatyuk6, M. Kellett7, T. Kibedi8, Kim Guinyun9, F .G. Kondev10, O. Lebeda11, A. Luca12, H. Naik13, Y. Nagai14, Nichols15, F. M. Nortier4, I. Spahn16, F. T. Tarkanyi17, M. Verpelli2 1Vrije Universiteit Brussel, Brussels, Belgium 2International Atomic Energy Agency, NAPC-Nuclear Data Section, Vienna, Austria 3 Instituto Tecnológico de Aeronáutica, Brazil 4Los Alamos National Laboratory (LANL), USA 5 Government College University, Lahore, Pakistan 6 Institute of Physics and Power Engineering (IPPE), Obninsk, Russia 7LNHB, CEA Saclay, France 8Australian National University, Canberra, Australia 9Kyungpook National University, Republic of Korea 10 Argonne National Laboratory, USA 11Nuclear Physics Institute, Rez, Czech Republic 12National Institute of Physics and Nuclear Engineering “Horia Hulubei”, Romania 13Bhabha Atomic Research Centre (BARC) Trombay Mumbai, India 14Japan Atomic Energy Agency (JAEA), Tokaimura Naka, Ibaraki-ken, Japan 15University of Surrey, Guildford, UK 16 Forschungszentrum Jülich (FZJ), Germany 17 Institute of Nuclear Research, Debrecen, Hungary
Notes: Thanks to organising committee and chairman, attendance

## Slide 19
Notes: Thanks to organising committee and chairman, attendance

## Slide 20
Notes: Thanks to organising committee and chairman, attendance

## Slide 21
Notes: Thanks to organising committee and chairman, attendance

## Slide 22
Notes: Thanks to organising committee and chairman, attendance

## Slide 23
Notes: Thanks to organising committee and chairman, attendance

## Slide 24
Notes: Thanks to organising committee and chairman, attendance

## Slide 25
Notes: Thanks to organising committee and chairman, attendance