## Slide 1
Richard Lanza1, Areg Danagulian1, Anna Erickson2, John Fisher1, Albert Foster4, Zach Hartwig1, Brian Henderson1, Igor Jovonovic3, Hin Lee1 ,T.D. MacDonald1, Amira Meddeb4, Jason Natress3, Roberts Nelson1,Buckley O’Day1,5, Zoubeida Ounaies4 and Paul Rose2
1Massachusetts Institute of Technology
2Georgia Institute of Technology
3University of Michigan
4Pennsylvania State University
5Air Force Institute of Technology
Generation and Detection of Neutrons and Monoenergetic Gamma Rays for Inspection for Nuclear Threats
INTERNATIONAL CONFERENCE ON APPLICATIONS OF NUCLEAR TECHNIQUES
CRETE, GREECE
JUNE 11 – 17, 2017

## Slide 2: What are we trying to do?
Develop a reliable means for the detection of shielded nuclear materials
Minimize dose
Increase reliability of detection by using multiple particles
Do it with a transportable system if possible

## Slide 3: Overview
Monoenergetic gammas for inspection
Using multiple energies for detection
Using neutrons
Accelerator technology

## Slide 4: Why use Monoenergetic Photons
An order of magnitude or more reduction in dose
Enhanced sensitivity in detection and verification
Lower requirements for shielding
The ability to reduce the size of the source part of the system by an order of magnitude or more while still meeting requirements for detection and identification of SNM
Flexibility in detection through radiography and active probing with the same device

## Slide 5: Transmission Issues
Evans, “Atomic Nucleus” 1955

## Slide 6
Transmission by Element

## Slide 7
Advantage of monochromatic

## Slide 8: Basic Approach
The fundamental approach is to generate both monoenergetic gamma rays and/or neutrons by means of low energy nuclear reactions.
  By selecting nuclear reactions with large positive Q values, small accelerators producing 3 to 20 MeV protons or deuterons can simultaneously produce fast neutrons and high energy ( > 10 MeV) monoenergetic gammas.
This multi-particle method images the SNM through shielding and also identifies it by inducing fission in the suspect material.
Use transmission imaging to locate high-Z materials
Use photofission and/or neutron induced fission as final check
Notes: Most reactions will involve light nuclei

## Slide 9: Some Features
Gamma ray energies are determined by nuclear physics and are not dependent on the energy of the beam
  Do not particularly need precise energy accelerator
  Compact accelerators are available commercially and are available in superconducting form
Neutrons available for final confirmation of SNM
  Intensities should enable rapid screening with subsequent ID
Going to higher power or more detectors is a COTS decision for even faster scanning
Notes: Gamma ray energies are not tunable, but there are a lot of choices. Neutron energies can be tuned

## Slide 10: Multi-Particle Interrogation Makes Effective SNM Shielding Difficult
R. Shefield, LANL

## Slide 11: Identifying SNM
Transmission measurement alone only identifies high-Z material
Use two approaches to distinguish 235U by detection of fission products
  Utilize photofission
  Probe with low energy neutrons (< 1MeV)

## Slide 12: What Nuclear Reactions to use?
One Example is 11B(d,n )12C
11B(d,n )12C Produces High-energy Neutrons And Gamma Radiation For Efficient Uranium Fission
12C* gamma lines found for >2 MeV deuterons have intense high energy-gamma lines at 4.4 and 15.1 MeV and less intense lines at 10.7 and 12.7 MeV.
The neutrons have a peak around 12 MeV and a broad distribution at lower energies.
Isotropic gamma distribution
Notes: Is isotropic bad? No in this case because all gammas are useable because we can use energy resolved detectors

## Slide 13: Other reactions considered
Early interest in possible low energy reactions for producing gammas, but these cross-sections are much smaller than (d,n) and require higher beam power
π
Notes: These were ideas to cut cost of accelerators

## Slide 14: Many Interesting Potential Reactions
Notes: Check physics journals from the 50’s and 60’s

## Slide 15: Gamma Production Rates
LA-UR-07-2724
Gamma Energy (MeV) | Yield (gammas/s/sr)
4.4 | 4 x 109
10.7 | 2 x 107
12.7 | 4 x 107
15.1 | 6.6 x 108
Notes: Note that this is the uncorrected spectrum as detected, not the actual spectrum

## Slide 16: 11B(d,n )12C
Data from Brandis et al (Crete 2010)
AIP Conference Proceedings 1336, 711 (2011)
Notes: Good news is many neutrons but bad news is more neutrons than gammas

## Slide 17: Gammas from 11B(d,n )12C
Notes: Note that efficiency of the HPGe drops with increasing energy. Is not corrected in this data

## Slide 18: Separating Actinides Using Multiple Lines
Marc Klasky and Richard Sheffield LANL

## Slide 19: Separating Actinides with Multiple Lines
Marc Klasky and Richard Sheffield LANL

## Slide 20: Summary Properties
Gamma lines are monoenergetic with energies determined by nuclear properties not accelerator
Source gammas are isotropic
System scanning can be speeded up by adding more detectors
Beam time structure allows for the use of energy sensitive detectors
Scatter can be rejected or utilized for imaging
3D imaging as an add-on
Neutron energies can be modified using p,n reactions with negative Q values
  50Cr(p,n)50Mn Q = -8.42 MeV
Notes: Pixel by pixel imaging is slow eg cargo container 2m x 6 m is 120K pixels

## Slide 21
Experimental System at MIT
Notes: A top-down view of a CAD representation of the multiple monoenergetic gamma
radiography experiment at MIT Bates

## Slide 22
Superconducting Cyclotron IONETIX ION-12SC
2 m

## Slide 23
Superconducting Cyclotron installed at MIT

## Slide 24
Team at MIT Bates Accelerator

## Slide 25: Related Papers at Crete17
Igor Jovanovic (U. Michigan, USA) Prompt and Delayed Fission Neutrons in Active Interrogation by Monoenergetic and Multimodal Radiation Sources (37)
Brian Henderson (MIT, USA) Detection of Special Nuclear Materials Using Multiple Monoenergetic Gamma Radiography (89)
Jason Nattress (U. Michigan, USA) Spectroscopic Multi-modal Material Identification using a Nuclear Reaction-Based Quasi Monoenergetic Source (36)
Paul Rose (Georgia Tech, USA) Searching for Special Nuclear Material with Discrete Energy Nuclear Reaction Based Sources and Cherenkov Detector Array (45)

## Slide 27: Photonuclear Cross-sections

## Slide 28: Double Lane Scanner
Detector array

## Slide 29
3D Imaging

## Slide 30: 3MeV D+ RFQ
RFQ accelerator, 3MeV
Focusing
quadrupoles
11B target
Beamline
RF
waveguide
d+ beam
d + 11B  12C + n + g
Notes: Here are some pictures of the actual setup.
The natural B target and radiation channel is shown in the top left
A typical cargo configuration in the top right, with side and front views
Bottom left shows a flood light being used to verify the detector placement by shining it through the two sets of collimators
Bottom right shows the detector array and Pb collimator and shielding.
We see an AutoCAD rendering of the experiment on the next slide.

## Slide 31
Spectrum from 12.5 MeV p on H2O
O lines with escape peaks

## Slide 32: Neutron probes
9 MeV Superconducting Cyclotron
  Generates 4.5 MeV d, or 9.0 MeV p
  Use the 9.0 MeV p in a (p,n) reaction
  e.g. 50Cr(p,n)50Mn Q = -8.42 MeV which results in En < 1 MeV, below fission threshold for 238U
~20 MeV Superconducting Cyclotron
  p on 12C generates only gammas below threshold ~19.5 MeV but have to watch for 13C
  Gammas and neutrons above threshold energy
Notes: 20 MeV might worry about C13

## Slide 33: Cyclotrons as Neutron Sources

## Slide 34: And more Potential Reactions…