## Slide 1: Investigating Artefacts Associated with β Particle Interactions in Charge Coupled Devices
Rosie Newton1 (r.newton1@lancaster.ac.uk)
Mike J. Scott2, Malcolm J. Joyce1
The 2017 International Conference on Applications of Nuclear Techniques - 15th June
1Engineering Dept., Lancaster University, UK
2BIC Technology Ltd., Liverpool, UK

## Slide 2: Overview
Introduction to the project
CCD operation
Identifying β clusters in CCD images
  Modelling
  Experimental
α particle research
Next steps

## Slide 3: Project introduction
Problem:
  In-situ detection of radioactive contamination – in particular of α radiation sources
Aims:
  Investigate potential of charge coupled devices (CCDs) for performing spectroscopy of α and β radiation
  Design and build a spectrometer for in-situ use

## Slide 4: Charge coupled devices (CCDs)
Sony ICX825AL
8.98 x 6.71 mm imaging size
  1392 x 1040 pixels
    6.45 x 6.45 μm size
More information:
https://www.sxccd.com/ultrastar-and-ultrastar-c
8.98mm
6.71mm
8.1cm
Notes: Interline CCD
If you include the interline thing make sure you explain it

## Slide 5: Charge coupled devices (CCDs)
Potential for detecting charged particles/ionising radiation
Particles create electron/hole pairs in the active region
  Collected by gate electrodes
Charge can spread into multiple pixels
  Trails
  Diffusion
  Blooming
e-
e-
e-
Active region
Gate structure
Substrate
Incoming particle/radiation
CCD basic single pixel structure

## Slide 6: CCDs – Previous research
α (241Am)
γ (241Am)
β (234Th)
[1] R. Newton, J. Dykes, M. J. Scott, and M. J. Joyce, “Alpha Contamination Assay , Dosimetry and Spectrometry Using Charge Coupled Devices.”, presented at IEEE Nuclear Science Symposium, Strasbourg, 2016.

## Slide 7: CCDs - Literature
[1] Aguilar-Arevalo, A. et al. Measurement of radioactive contamination in the high-resistivity silicon CCDs of the DAMIC experiment. J. Instrum. 10, P08014–P08014 (2015)
[2] Estrada, J . et al. Plasma effect in silicon charge coupled devices (CCDs). Nucl. Instruments Methods Phys. Res. Sect. A Accel. Spectrometers, Detect. Assoc. Equip. 665, 90–93 (2011).
Portion of a DAMIC image [1]
Picture of an exposure of the DECam CCD to cosmic rays. Muons, alphas, electrons and low energy photons can be distinguished by their signatures on the CCD. [2]
Example of a plasma (left) and bloomed (right) alpha detection [1]
Notes: Mention all the prominent things

## Slide 8: β-particle sources
Two sources available for use:
  137Cs Emax: 512 keV
  60Co Emax: 310 keV
These will be used for both simulation and experimental research
Aim:
  Investigate the differences in the expected and actual pixel clusters for each source
  Look for a difference relating to the energies of the β particles

## Slide 9: Modelling – CASINO
Software: CASINO (monte CArlo SImulation of electroN trajectory in sOlids) [1]
  [1] H. Demers, et al, “Three-dimensional electron microscopy simulation with the CASINO Monte Carlo software.,” Scanning, vol. 33, no. 3, pp. 135–46, May (2011) . http://www.gel.usherbrooke.ca/casino/
30 tracks, 512 keV electrons

## Slide 10: Modelling – CCD structure
Pixel structure used:
  2x2 binning to match software
  Pixel length and width from CCD datasheet
  Active area and substrate depth based on typical examples from literature (60 μm each) [1-3]
  No gate structure – previously shown to be negligible for these β particle energies [4]
[1] Li, F. & Nathan, A. CCD Image Sensors in Deep-Ultraviolet: Degradation Behavior and Damage Mechanisms. (Springer Science & Business Media, 2006).
[2] Burke, B., Jorden, P. & Paul, V. U. CCD technology. Exp. Astron. 19, 69–102 (2006).
[3] Aguilar-Arevalo, A. et al. Measurement of radioactive contamination in the high-resistivity silicon CCDs of the DAMIC experiment. J. Instrum. 10, P08014–P08014 (2015).
[4] R. Newton, J. Dykes, M. J. Scott, and M. J. Joyce, “Alpha Contamination Assay , Dosimetry and Spectrometry Using Charge Coupled Devices.”, presented at IEEE Nuclear Science Symposium, Strasbourg, 2016.

## Slide 11: Modelling – 60Co and 137Cs
CASINO output for 310 keV e- (60Co)
CASINO output for 512 keV e- (137Cs)
20 pixels (129µm)
20 pixels (129µm)
60µm
60µm
20 pixels (129µm)
20 pixels (129µm)
60µm
60µm
10,000 simulated electrons (30 shown)
All regions are silicon

## Slide 12: Modelling - 60Co and 137Cs
137Cs peak: 2 pixels
60Co peak: 2.5 pixels
60Co has a greater percentage of larger clusters

## Slide 13: Experimental setup
CCD in contact with source
Aimed for similar counts to avoid overlapping clusters:
  60Co: 100s - 26,003 counts
  137Cs: 20s - 28,056 counts
Clusters are any pixels connected horizontally, vertically or diagonally

## Slide 14: Experimental results
137Cs
1s exposure
Image sections: 146×114 pixels
(4.5% of total image size)
60Co
5s exposure
Notes: 4.5%

## Slide 15: Experimental results
Lognormal fits well but peak shifted to smaller 1 pixel clusters in both cases
Smaller clusters dominated by γ radiation
Notes: Include the screening – saw gamma but none of the longer streaks
Half mm plastic on source check in casino for attenuation

## Slide 16: Comparison of results
CASINO results (β particles only)
Experimental results (β and γ)
Notes: Equation between energy and scattering

## Slide 17: Po-210 α particle source
Single α particle energy: 5.31 MeV
No β/γ radiation
Half life: 138 days
SRIM (Stopping and Range of Ions in Matter) simulation data [1]
  [1] Ziegler, J. F., Ziegler, M. D. & Biersack, J. P. SRIM – The stopping and range of ions in matter (2010). Nucl. Instruments Methods Phys. Res. Sect. B Beam Interact. with Mater. Atoms 268, 1818–1823 (2010). http://www.srim.org/
Notes: Po not used often – check
Includee assumptions

## Slide 18: Po-210 α particle source
Experimental data, streaks counted if they consist of more than 6 pixels in length. Total number of streaks: 1625
210Po (30s) image section
208x144 pixels, 8.3% of total image
Notes: “no detected radioimpurities”

## Slide 19: Summary
CCDs show potential for spectroscopy of radioactive contamination
CCD response to β radiation has been investigated
  Simulations show lower energy β particles scatter more and hence have longer tracks
  Experimentally, there is a small difference seen between the responses to 60Co and 137Cs, however the smaller clusters are dominated by γ radiation
Investigations into α clusters and blooming have started with the 210Po source

## Slide 20: Future research
Continue β investigations
  Separate the responses from β and γ radiation
  Use a β particle source with a more significantly different energy
Continue research with α particle source
  Investigate response to different α particle energies
Develop β and α identification from mixed sources

## Slide 21: Acknowledgements
NGNCDT
Thank you for listening!
r.newton1@lancaster.ac.uk